# Broadly Reconfigurable and Expandable Automation Device (BREAD) – Slice Datasheet: 20A Current Sensor Slice (SLC-CR20)
By: Nicholas Whisman (ngwhisma@mtu.edu) – Revision 0, on 17. May 2021
## Short Device Description
This slice acts as a current sensor, and is rated for up to ±20 Amps. The sensor outputs a voltage signal linearly related to the current flowing through the chip, at an approximate resolution of 100 mV / Amp.
## Quick Information
Device at a Glance
Short title	20A Current Detector
Part #	SLC-CR20
Repository Link	Link to OSF or other repository
Academic Paper DOI	DOI link to published paper
Device Cost	Monetary cost of the device
Assembly Difficulty	Medium. Millable.
Application Area	Power Analysis, Controls

Device Connections
Current Input Screw Terminals
Pin #	Description	Rating
J2	Sizeable blade connector for current channel throughput. Positive lead on the right.	50A+
J3	Sizeable blade connector for current channel throughput. Positive lead on the right.	50A+
J4	Sizeable blade connector for current channel throughput. Positive lead on the right.	50A+
J5	Sizeable blade connector for current channel throughput. Positive lead on the right.	50A+
J6	Sizeable blade connector for current channel throughput. Positive lead on the right.	50A+
J7	Sizeable blade connector for current channel throughput. Positive lead on the right.	50A+
J8	Sizeable blade connector for current channel throughput. Positive lead on the right.	50A+
J9	Sizeable blade connector for current channel throughput. Positive lead on the right.	50A+

## Commands
Setup (no significant returns)
Byte: Address	Bit: 1	Float: Target Temp	Float: Ramp Rate (d/m)
Read Current (returns the current through the selected channel)
Byte: Address	Bit: 0	Float: 0	Float: 0

## Schematic

Figure 1: BREAD Connection Pins + Power Capacitors
Figure 2: Arduino Nano

Figure 3: One of four identical current sensing channels

## Bill of Materials
Designator	Description	Quantity	Cost / part	URL
U1-4	20A Current Sensor Chip	4	5.68	https://www.digikey.com/en/products/detail/allegro-microsystems/ACS723KMATR-20AB-T/5225377
J2-J9	Blade Connectors	8	0.37	https://www.digikey.com/en/products/detail/w%C3%BCrth-elektronik/7474966/9488016
C1-2	1206 Packaging 10 µF Capacitor	2	0.64	https://www.digikey.com/short/qfrbqfhd
A1	Arduino Nano	1	22.00	https://www.digikey.com/en/products/detail/arduino/A000005/2638989
J1	01x10 Female Header Pins	1	0.79	https://www.digikey.com/short/23bfwwjh

## Construction & Fabrication
List any tools that are required and short guide on the order which parts should be soldered / assembled. Be sure to note any specialized methods and point out components that may easily be soldered in the incorrect orientation. Additionally include at least one picture of the assembled board (include both sides if there are components on both sides).
[Image of the assembled Circuit Board]
Fig #. Subtitle should go here.
## Configuration & Calibration
Include a list of default jumper and potentiometer positions:
Hardware Positions
- Turn P1 to be roughly 50%
- Turn P2 to be completely closed (turn clockwise until potentiometer clicks)
- Place a jumper to short out J3. Etc…
Detail any key parameters the end-user may want to adjust in the firmware, and if there are any special instructions before programming the Slice.
Tools Required For Calibration
- An oscilloscope with at least 15Mhz sampling
- A multimeter. Etc…
List all of the tools / instruments required for calibration. Provide a detailed & step by step guide on how to calibrate (or validate) each unique type of channel on the card. Include what variables in the firmware may need to be adjusted (and when). Attach a wiring diagram for each relevant calibration circuit.
[Image of the calibration circuit]
Fig #. Subtitle should go here.
## Usage & Constraints
List the relevant constraints for each type of channel on the card. These parameters may be quantities like max current, max voltage, frequency, sampling frequency, etc.
List an example wiring diagram of the slice in use, as well as some suggested applications
[Image of the example usage wiring diagram]
Fig #. Subtitle should go here.
## General Comments on Slice
This section is intended as a catch-all for any topics that are relevant to the Slice that don’t fit in any other category.
## Revision Notes
Rev 0 – Initial document release (DATE HERE)