# Broadly Reconfigurable and Expandable Automation Device (BREAD) – Slice Datasheet: Servo Motor Control Slice (SLC-SERV)
By: Nicholas Whisman (ngwhisma@mtu.edu) – Revision 0, on 18. May 2021
## Short Device Description
This device controls up to 5 Servo motors. As Servo motors have internal feedback control systems, this system thus has no feedback path.
## Quick Information
Device at a Glance
Short title	Servo Motor Control Slice
Part #	SLC-SERV
Repository Link	Link to OSF or other repository
Academic Paper DOI	DOI link to published paper
Device Cost	Monetary cost of the device
Assembly Difficulty	Easy, Millable
Application Area	Robotics, Controlling Machinery

Device Connections
J2 – Servo Motor 1
Pin #	Description	Rating
1	PWM to Servo	N/A
2	Voltage Input	Varies by Motor. Terminal can only support 10-15A
3	GND	N/A

J3 – Servo Motor 2
Pin #	Description	Rating
1	PWM to Servo	N/A
2	Voltage Input	Varies by Motor. Terminal can only support 10-15A
3	GND	N/A

J4 – Servo Motor 3
Pin #	Description	Rating
1	PWM to Servo	N/A
2	Voltage Input	Varies by Motor. Terminal can only support 10-15A
3	GND	N/A

J5 – Servo Motor 4
Pin #	Description	Rating
1	PWM to Servo	N/A
2	Voltage Input	Varies by Motor. Terminal can only support 10-15A
3	GND	N/A

J6 – Servo Motor 5
Pin #	Description	Rating
1	PWM to Servo	N/A
2	Voltage Input	Varies by Motor. Terminal can only support 10-15A
3	GND	N/A

J7 – Power Select
Pin #	Description	Rating
1	Power Output Pin	MUST connect one of the below to this pin.
2	Custom Power Input	N/A
3	Standard 12V	N/A

J8 – Custom Power Input
Pin #	Description	Rating
1	V +	N/A
2	GND	N/A

## Commands
Write Angle (no significant returns)
Byte: Address	Bit: 1	Float: Target Temp	Float: Ramp Rate (d/m)
Set Up (no significant returns)
Byte: Address	Bit: 0	Float: 0	Float: 0

## Schematic

Figure 1: BREAD Connection Port and Power Capacitors

Figure 2: Arduino Nano
Figure 3: One of five identical Servo connection ports

Figure 4: Power Select Pins

Figure 5: Custom Power Input Port
## Bill of Materials
Designator	Description	Quantity	Cost / part	URL
J8	01x02 1/10” Pitch Terminal Block	1	1.27	https://www.digikey.com/short/792dvv77
J7	01x03 1/10” Pitch Connector Pins	1	0.27	https://www.digikey.com/short/2j42vf3d
J2-J6	01x03 1/10” Pitch Terminal Block	5	2.06	https://www.digikey.com/short/18bph2rj
J1	01x10 Female Header Pins	1	0.79	https://www.digikey.com/short/23bfwwjh
C1-2	1206 Packaging 10 µF Capacitor	2	0.64	https://www.digikey.com/short/qfrbqfhd
A1	Arduino Nano	1	22.00	https://www.digikey.com/en/products/detail/arduino/A000005/2638989

## Construction & Fabrication
List any tools that are required and short guide on the order which parts should be soldered / assembled. Be sure to note any specialized methods and point out components that may easily be soldered in the incorrect orientation. Additionally include at least one picture of the assembled board (include both sides if there are components on both sides).
[Image of the assembled Circuit Board]
Fig #. Subtitle should go here.
## Configuration & Calibration
Include a list of default jumper and potentiometer positions:
Hardware Positions
- Turn P1 to be roughly 50%
- Turn P2 to be completely closed (turn clockwise until potentiometer clicks)
- Place a jumper to short out J3. Etc…
Detail any key parameters the end-user may want to adjust in the firmware, and if there are any special instructions before programming the Slice.
Tools Required For Calibration
- An oscilloscope with at least 15Mhz sampling
- A multimeter. Etc…
List all of the tools / instruments required for calibration. Provide a detailed & step by step guide on how to calibrate (or validate) each unique type of channel on the card. Include what variables in the firmware may need to be adjusted (and when). Attach a wiring diagram for each relevant calibration circuit.
[Image of the calibration circuit]
Fig #. Subtitle should go here.
## Usage & Constraints
List the relevant constraints for each type of channel on the card. These parameters may be quantities like max current, max voltage, frequency, sampling frequency, etc.
List an example wiring diagram of the slice in use, as well as some suggested applications
[Image of the example usage wiring diagram]
Fig #. Subtitle should go here.
## General Comments on Slice
This section is intended as a catch-all for any topics that are relevant to the Slice that don’t fit in any other category.
## Revision Notes
Rev 0 – Initial document release (DATE HERE)